## Slide 1: Analyzing the Best Fracker Inventors Program
Vee Lee Koh (PGE), Kushal Pachchigar (CS),
Anjali Sridharan (ChemE), Kaylee Trevino (ECE)

## Slide 2: Presentation Flow
Problem Statement
Efficiency Metrics
Conclusion
Principal Component Analysis

## Slide 3: Problem Statement
Finding out, at any given moment, which one of the 5 Eagle Ford frac crews is the best performer
Creating an equitable ranking system

## Slide 4: How Did we Define “Best” Fracker in Our Analysis?
Efficiency metrics:
  Average Pump Time
  Time Interval between Stages
  Mobilization Time
  Demobilization time
Grouped by:
  Service Company
  Project Type (Initial Completion vs Recompletion)
  Well

## Slide 5: Number of Wells by Service Company
Service Company | # Completion Wells | # Recompletion Wells
A (04) | 192 | 28
B (05) | 67 | 12
C (07) | 8 | 1
D (03) | 33 | 7
E (02) | 87 | 10

## Slide 6
Average Pump Time
Average Time to Pump Each Stage /
10 MM lbs Proppant / 10 MM bbl Fluid
Assumptions: Only considered stages which pumped more than 500 lbs proppant, 500 bbl fluid and 12 stages; Fluid and proppant type neglected

## Slide 7: Completions Recompletions P-value P-value
t-test Hypothesis Testing: Average Pump Times by Company
Notes: Using t-test for hypothesis testing as we're comparing the means of average pump time distributions of different companies. Due to some companies having less data (n<30), t-test is suitable. t-test also approaches z-test as number of data increases.
t-test assumes Gaussian distribution but data doesn't look Gaussian
  Performed Bootstrap to prove that data approaches Gaussian with resampling (Central Limit Theorem)
Assume unequal variance
Two tailed test with 95% confidence

## Slide 8: Average Pump Time for Initial Completions Results Average Pump Time for Recompletions

## Slide 9
Time Interval Between Stages
Assumption: Diversion method (plug type) neglected

## Slide 10: Time per Interval for Completions Time per Interval for Recompletions Results

## Slide 11
Mobilization Time
Assumption: Filter out times greater than 1 week

## Slide 12: Mobilization Time for Completions Results Mobilization Time for Recompletions

## Slide 13
Demobilization Time
Assumption: Filter out times greater than 1 week

## Slide 14: Demobilization Time for Completions Results Demobilization Time for Recompletions

## Slide 15
Initial Completions
Recompletion
All Metrics by Company
Notes: The shorter the time, the better
For Completions, neglecting C (due to limited sampling) A & B perform better in 3 out of 4 metrics than C & D
For Recompletions, neglecting companies which have less than 10 wells (C & D), A, B & E perform best on different metrics
Compare the two projects - Recompletions has higher average pump time than initial completions but shorter time intervals btwn stages

## Slide 16
Principal Component Analysis
Combining the four metrics to create an
efficiency score

## Slide 17
PCA Overview
Credits to Dr. Prycz (PGE) - Figure taken from Subsurface Machine Learning course
Notes: Standardize metrics
Fit the PCA model with metrics dataframe to get component loadings → analyze to see which metrics strongly influence each PC
Also look at variance explained by each PC → make a decision on which PC to drop to reduce the dimensionality
Product will give me the PC score (Efficiency scores)

## Slide 18
PCA - Initial Completions
Component
Loadings
Scree Plot of Variance Explained
Notes: % of variance explained by PC1 thru PC4 = [67 23 9 0]

## Slide 19
COMPANY | # WELL | 1st PC SCORE
A | 192 | 0.175514
B | 67 | 0.264578
C | 8 | 2.841186
D | 33 | -1.575974
E | 87 | -1.705304
PCA Completions Efficiency Score
The higher the PC score,
the higher the efficiency

## Slide 20: Conclusions
Next steps:
Group by fluid and plug type
Outlier detection of time interval between stages
Perform cost analysis (Efficiency / Cost)
For initial completions, C neglected due to limited sampling
For recompletions,
C & D neglected due to limited sampling
EFFICIENCY METRICS | BEST IN INITIAL COMPLETIONS | BEST IN RECOMPLETIONS
AVERAGE PUMP TIME | B, A | B, E
INTERVAL BETWEEN STAGES | B, A | E, A
MOBILIZATION TIME | D, B | A, B
DEMOBILIZATION TIME | A, B | A, E
OVERALL | B & A | A & E

## Slide 21
Use Cases for COP

## Slide 22
Thank You for the Opportunity!

## Slide 23
Appendix

## Slide 24
Efficiency Metric Values - Initial Completions
COMPANY | WELL | PUMP TIME PER STAGE/PROP/FLUID | TIME INTERVAL PER INTERVAL | MOBILIZATION TIME | DEMOBILIZATION TIME
A | 192 | 44.138716 | 6.501828 | 32.988421 | 22.769035
B | 67 | 39.820412 | 5.976615 | 31.283333 | 26.147264
C | 8 | 21.997736 | 4.657350 | 45.581250 | 28.381250
D | 33 | 53.946075 | 6.945747 | 28.355556 | 33.392929
E | 87 | 59.284559 | 8.261611 | 33.728544 | 28.989535

## Slide 25
Efficiency Metric Values - Recompletions
COMPANY | WELL | PUMP TIME PER STAGE/PROP/FLUID | TIME INTERVAL PER INTERVAL | MOBILIZATION TIME | DEMOBILIZATION TIME
A | 28 | 173.004308 | 3.580470 | 40.930247 | 17.968000
B | 12 | 109.734543 | 3.825480 | 42.718056 | 21.730556
C | 1 | 135.671307 | 3.524603 | 31.950000 | 14.500000
D | 7 | 184.377920 | 0.711492 | 55.913889 | 24.736667
E | 10 | 147.435767 | 2.381388 | 61.708333 | 20.125000

## Slide 26
Bootstrap on Company C’s Completions Data

## Slide 27
COMPANY | WELL | 1st PC SCORE | PUMP TIME PER STAGE/PROP/FLUID | TIME INTERVAL PER INTERVAL | MOBILIZATION TIME | DEMOBILIZATION TIME
A | 192 | 0.175514 | 42.474607 | 6.351145 | 34.922656 | 27.799994
B | 67 | 0.264578 | 41.783011 | 6.291528 | 35.194259 | 27.730977
C | 8 | 2.841186 | 21.775244 | 4.566805 | 43.051706 | 25.734319
D | 33 | -1.575974 | 56.075186 | 7.523551 | 29.581439 | 29.157252
E | 87 | -1.705304 | 57.079450 | 7.610121 | 29.187044 | 29.257471
PCA - Initial Completions
What the PC scores translate to:

## Slide 28
PCA - Recompletions
Notes: % of variance explained by PC1 thru PC4 = [68 20 7 3]

## Slide 29
PCA - Recompletions
What the PC scores translate to:
COMPANY | WELL | 1st PC SCORE | PUMP TIME PER STAGE/PROP/FLUID | TIME INTERVAL PER INTERVAL | MOBILIZATION TIME | DEMOBILIZATION TIME
A | 28 | -0.571049 | 143.894124 | 3.179574 | 43.460807 | 18.832882
B | 12 | -1.024871 | 139.006111 | 3.477503 | 40.930991 | 18.054726
C | 1 | -2.043417 | 128.035585 | 4.146167 | 35.253139 | 16.308253
D | 7 | 2.699430 | 179.119727 | 1.032540 | 61.691998 | 24.440684
E | 10 | 0.939907 | 160.168299 | 2.187648 | 51.883590 | 21.423678

## Slide 30
PCA - Completion vs Recompletion

## Slide 31
Completions

## Slide 32
Recompletions

## Slide 33: Time per Interval for Completions Time per Interval for Recompletions Results for Time Interval Between Stages